## Slide 1
LEAN SIX SIGMA TOOLKIT

## Slide 2: What is this Toolkit for?
If you’re reading this, you probably already know how important continuous improvement is for the long-term success of any company. This toolkit is designed to help you get a better understanding of Lean Six Sigma, the methods and tools that come with this framework for continuous improvement.
In this PowerPoint Presentation, we’ll provide you with actionable tools and templates, as well as some additional explanations to help you grasp the concepts better. You can find more useful information behind the links and in the presentation slide notes.
How to use it?
This presentation will walk you through the key parts. Most slides have additional notes that explain the tools and methods in more detail. For the detailed take on Lean Six Sigma, please refer to our dedicated article:
For more information on innovation management and continuous improvement in general, please refer to our blog.
PLEASE NOTE: This Toolkit is a starting point. Getting results will always take time and effort. These are just some of the possible tools you can use in Lean Six Sigma. Given their level of complexity, if you are new at LSS, we advise you to explore in much detail each tool before taking it into use.
Notes: For each phase we listed a set of tools that can be used in a Lean Six Sigma project.
You don’t have to use all of them. Choose what you find most suitable for your type of project and needs.
Some of the tools can be used in more than one stage. For example, 5S can be used both in the Define and Improve phases of the DMAIC model. We included all the details and templates only under the Define stage, so the slides won’t be repetitive.

## Slide 3: Table of Contents
Define - Project Charter - SIPOC Diagram - Value Stream Map
- Voice of the Customer analysis - Jobs to Be Done - 5S
Measure - Data Collection Plan - Measurements for LSS: DPU, DPMO, RTY, Cycle Time, COPQ
- Visualizing your data: Process Map, Histogram, Pareto Charts - Gemba Walk
Analyze - Quantitative: Regression analysis, Histogram, Pareto Charts - Qualitative: 5 Whys, FMEA, Fishbone Diagram, XY Matrix
Improve - Brainstorming and idea generation - Design for Experiments (DOE)
- How Might We Statements (HMW) - FMEA
Control - Control Plan - Statistical Process Control (SPC) - Standard Operating Procedures (SOP)

## Slide 4
Customer focus
Lean Six Sigma Principles
Continuous Improvement
Data-driven decision making
Structured problem solving
Standardization
Leadership commitment

## Slide 5
Define
Measure
Analyze
Improve
Control
Objective
Knowledge
Define the problem and set up project goals
Understanding of project scope, goals, and objectives. outcomes.
Skills
Tools
Problem definition, stakeholder management, project scoping.
Project Charter,
SIPOC diagram, Voice of the Customer (VOC) analysis, JBTD
Measure current performance & look for potential causes of the problem
Data collection methods, basic descriptive statistics.
Data gathering, process mapping, measurement systems.
Data collection plan, Gage R&R study, Process Map, Histogram, Pareto Chart.
Analyze the data and identify the root cause of the problem
Statistical analysis techniques, root cause analysis methods.
Identifying patterns, analyzing data, finding root causes.
Fishbone Diagram, 5 Whys, Scatter Plot, Regression Analysis. Quantitative and Qualitative tools
Develop solutions to address the root causes
Creativity techniques, process redesign concepts.
Generating solutions, piloting changes, evaluating alternatives.
Brainstorming, DOE, Simulation, How might we statements, idea challenges
Monitor and continuously improve
Process control concepts, mistake-proofing methods.
Implement, sustain improvements, develop control plans.
Control Plan, Statistical Process Control (SPC) charts, Standard Operating Procedures (SOPs)
Lean Six Sigma
DMAIC framework

## Slide 6
Project Charter
SIPOC Diagram (Suppliers, Inputs, Process, Outputs, Customers)
Process Mapping
  Value Stream Map
VoC (Voice of the Customer) analysis
JTBD (Jobs To Be Done)
5S
Tools
DEFINE
In this phase you:
Define the issues and action plan necessary to attain the desired results towards process improvement
Define the issues and improvement activity’s objectives
Understand the problem as a whole and understand the customer’s preferences
Define a problem statement and look at the data to check if the reported issue is relevant
Notes: Project charter: outlines the scope, objectives, and key details of a project. It serves as a foundational reference and guide for the project team, stakeholders, and sponsors throughout the project's lifecycle. The project charter provides clarity and alignment on the project's purpose, goals, and expected outcomes.
SIPOC Diagram: The SIPOC diagram (Suppliers, Inputs, Process, Outputs, Customers) outlines the high-level components of a process, including the suppliers, inputs, process steps, outputs, and customers. It helps define the boundaries of the process and identify key elements.
Value Stream Map: A tool specific to Lean methodology, it visualizes the entire value stream, including both value-adding and non-value-adding activities, to identify areas for improvement.
Voice of the Customer (VoC) analysis is a systematic process of capturing and understanding customer feedback, needs, expectations, and preferences regarding a product, service, or process. It involves gathering insights directly from customers to ensure that the offerings meet their requirements and deliver value.
JTBD (Jobs To Be Done) framework provides insights into why customers make purchasing decisions and how products or services can be improved to better address their needs. By integrating it into the DMAIC process, you can ensure that process improvements are not only data-driven but also customer-centric. It helps avoid assumptions and focuses efforts on creating solutions that genuinely address customers' fundamental needs, enhancing the overall effectiveness of the improvement efforts.

## Slide 7
Why you need an improvement project? Highlight the losses that come from current process, and possible gains by implementing the improvements.
Business case
Project Charter
Project Name:
Date (Last Revision):
Describe the problem and opportunities in measurable terms. How often the problem occurs, where, and who’s impacted?
Project scope
Process Start Point
Process End Point
In Scope
Out of Scope
Opportunity statement (high level problem statement)
Defect definition
What is the improvement? When should it be finalized?
Goal statement (SMART objectives)
Expected savings
Task/Phase
Name
Project plan
Team
Role
Commitment %
Start Date
End Date
Actual End
Prepared by:
Approved by:
Notes: Project charter: outlines the scope, objectives, and key details of a project. It serves as a foundational reference and guide for the project team, stakeholders, and sponsors throughout the project's lifecycle. The project charter provides clarity and alignment on the project's purpose, goals, and expected outcomes.

## Slide 8
Value Stream Mapping
Map the process
Find and eliminate waste
Map improvements and future process
Implement the new process
The value stream mapping (VSM) has four major steps meant to help you identify areas of improvement.
Notes: Value Stream Mapping (VSM) is typically used in the "Define" and "Measure" stages of the DMAIC (Define, Measure, Analyze, Improve, Control) process in Six Sigma.
In the Define stage, the focus is on understanding the current state of the process, defining its scope, and identifying the main problems or inefficiencies.
In the Measure stage, data is collected to quantify the current state of the process and identify the extent of the issues. The VSM created in the Define stage provides a reference for understanding the process flow and helps identify key process metrics that need to be measured. The Measure stage also involves gathering data on cycle times, lead times, processing times, and other relevant process parameters to establish a baseline for improvement.
While Value Stream Mapping is particularly useful in the Define and Measure stages, its insights continue to inform the subsequent stages of Analyze, Improve, and Control. It helps guide the identification of root causes, the development of improvement strategies, and the establishment of control measures to sustain improvements over time.
A value stream map is a comprehensive visual tool that depicts the entire end-to-end process, from the initial raw materials to the final customer delivery. It illustrates both value-adding and non-value-adding activities, allowing organizations to identify opportunities for waste reduction, process optimization, and overall efficiency improvement.
VSM provides an overview of the entire value stream, highlighting areas where changes can have the most significant impact.

## Slide 9
The Value Stream Mapping process
1. Identify the problem
2. Choose the team
3. Define the scope
4. Create a timeline
5. Add project data
6. Map your value stream
7. Analyze the current map
8. Design the new map
9. Implement the new map
Notes: Identify the problem Brainstorm and ask questions to identify inefficiencies.
Choose the team Get together people with different expertise to provide a wide variety of skills and perspectives into possible solutions.
Define the scope Choose on what area of the project to focus on.
Map your value stream Map the process on three levels. Visualize the product, information and time flows.
Add project data Include relevant metrics to help you compare data and get accurate insights on time, quality, and quantity.
Create a timeline Set a clear timeline to get a better sense of the lead time and cycle time
Analyze the current map Notice areas that need improvement as you build the current state map.
Design the new map Start working on the future state map where you include elements for areas that need improvement.
Implement new map Apply the solutions from the new map to the work process.

## Slide 10
Value Stream Mapping example
Information flow
Product flow
Time flow
Production
Control
Milling
Supplier
Market forecast
Recycling
CT: 2 min
Shipping
Daily schedule
Total lead time: 60 days
Daily order
Customer
2 people
C/O: 3 hr
Welding
CT: 1 min
3 people
C/O: 2 hr
Painting
CT: 7 min
2 people
C/O: 4 hrs
Assembly and production ´
CT: 2 min
3 people
C/O: 30 hrs
Value added time: 16 min
5d
10d
12d
8d
2min
4min
7min
3min
25d
Weekly schedule
Weekly Delivery Plan
Notes: A value stream map that runs in circle because the customer demand feeds both the supply and production chain.

## Slide 11
Purpose of the process:
SIPOC diagram Example for restaurant food preparation.
Interrelated processes
Process owner:
KPIs and measurement frequency
Suppliers
Inputs
Process
Outputs
Customers
Process breakdown
What are the key outputs?
Who are the recipients?
Notes: A SIPOC diagram focuses on capturing the high-level components and interactions of a process. It provides a broader perspective on the process and its relationship to external entities.
The SIPOC diagram is structured around five key elements: Suppliers, Inputs, Process, Outputs, and Customers. It provides a concise overview of who contributes, what is involved, and who benefits from the process.
SIPOC diagrams are usually less detailed than functional diagrams. They provide a simplified representation of the process's key elements without delving into the specific steps or functions.
To create a SIPOC diagram:
1. Map The Process. Break down the process into up to five high-level activities comprising the business process.
2. Identify The Process Outputs. Include up to five key process benefits.
3. Identify The Customers. Determine the recipients of the process outputs – external or internal.
4. Determine The Process Inputs. Map the key inputs necessary for the process completion.
5. Identify The Suppliers. Determine the suppliers of the inputs required by the process.
Once the diagram is complete, it has to be shared with project leaders and stakeholders for its verification before implementation.
**For more transparency and better collaboration, you can implement something similar in Viima using the custom fields. Sign up for free to learn how you can get started. https://app.viima.com/signup
All users have free access to our extensive knowledge base which helps you get started through illustrated, step by step instructions on how to configure and use the software.

## Slide 12
Notes: This is one example of a VoC matrix.
There are several Voice of the Customer (VoC) tools available that can help you gather, analyze, and act upon customer feedback and insights. The one you choose comes down to your specific needs, the size of your organization, complexity of feedback needs, integration capabilities, reporting and analysis features.
You can try Viima for free to collect customer insights and data. https://www.viima.com/voice-of-the-customer
Other VoC tools you can consider:
SurveyMonkey: A user-friendly survey tool that enables organizations to create and distribute surveys to collect feedback from customers. It offers customizable templates and robust reporting features. Medallia: Offers a wide range of VoC solutions, including surveys, social media monitoring, and text analytics. It helps businesses understand customer sentiment and track their experiences across different touchpoints.
Wootric: Focuses on real-time customer feedback collection through NPS surveys, enabling organizations to gather insights and take immediate actions to improve customer experiences.
7 steps for VoC analysis:
Step 1: Collect Customer Feedback: Gather customer feedback from various sources such as surveys, interviews, focus groups, customer service interactions, and online reviews. Compile both qualitative and quantitative data.
Step 2: Categorize Customer Inputs: Organize the collected feedback into categories that represent different customer needs, expectations, and preferences. These categories could be related to product features, quality, service, convenience, and more.
Step 3: Prioritize Customer Needs: Rank or prioritize the identified customer needs based on factors such as their importance, frequency of occurrence, and impact on customer satisfaction. This helps in focusing efforts on addressing the most critical needs first.
Step 4: Define Specific Criteria: For each prioritized customer need, define specific, measurable criteria that can guide improvement efforts. These criteria should be
clear, concise, and aligned with the corresponding customer need.
Step 5: Assign Metrics: Identify key performance indicators (KPIs) or metrics that will be used to measure the performance of the process or product in relation to each customer need. These metrics should be quantifiable and relevant.
Step 6: Develop Improvement Plans: Based on the VoC matrix, create action plans to address the gaps between customer needs and the current state of the process or product. Determine how each need can be met through process enhancements, feature additions, or service improvements.
Step 7: Monitor and Update: Establish mechanisms to continuously monitor customer feedback and update the VoC matrix accordingly. Regularly review and adjust improvement initiatives based on changing customer preferences and new insights.
To enhance your understanding of customer needs and improve customer experiences you can also create a VoC matrix.
Creating a Voice of the Customer (VoC) matrix can be used to categorize and prioritize customer feedback and needs based on their impact on customer satisfaction and the effort required to address them.
Usage: It's a manual approach that involves analyzing customer feedback and organizing it into categories and priorities.
Benefits: Provides a structured way to understand customer needs, aligns the team around priorities, and guides improvement efforts.
Limitations: Manual process, may not provide real-time insights, lacks features for data collection and sophisticated analysis.

## Slide 13
1. Define
Anxiety
Version:
Job statement (Verb + object + context)
The Jobs To Be Done Canvas
Project:
Job executor (who’s your end user):
2. Locate
3. Prepare
4. Confirm
5. Execute
6. Monitor
7. Modify
8. Conclude
Job map
Progress
Habits
Problem
Forces of progress
Emotional
Job roles
Functional
Social
Notes: Jobs To Be Done (JTBD) explains how and why customers “hire” or pull certain products or services into their life. It’s not about a specific task or activity that triggers their action, but it uncovers the customers’ desire to make progress, in given circumstances.
Jobs To Be Done supports innovation by looking into why and how someone decides to hire a product or service and creates the setting to find better fitted solutions that create value for customers.
We wrote an extensive guide on the topic, which you can discover here: https://www.viima.com/blog/jobs-to-be-done
For the dedicated toolkit for JTBD, go here to download it for free: https://www.viima.com/jobs-to-be-done-toolkit

## Slide 14
Sort
(Seiketsu)
Separate needed items from unneeded and eliminate the later
Set in
order
(Seiri)
Keep needed items in the correct place to allow easy and fast retrieval
Shine
(Seiton)
Standardize
(Seiso)
Create a consistent approach with which tasks and procedures are done
Keep the workplace swept and clean
Sustain
(Shitsuki)
Habit to maintain established processes
The 5S Framework
Notes: The 5S methodology can be integrated with Lean Six Sigma to enhance process efficiency, organization, and continuous improvement efforts. While Lean Six Sigma focuses on reducing variability and improving quality, the 5S methodology complements it by creating a well-organized and standardized work environment.
Here's how you can integrate 5S principles into Lean Six Sigma:
1. Sort (Seiri): Incorporate this principle to identify and prioritize problems or process inefficiencies in the Define stage of DMAIC. Sort through data to determine which issues have the highest impact and should be addressed first.
2. Set in Order (Seiton): During the Define and Measure stages, apply this principle to organize and structure data related to the identified issues. Ensure that relevant information is readily accessible for analysis.
3. Shine (Seiso): Maintain a clean and organized work environment throughout the entire Lean Six Sigma process. A clutter-free workspace aids in accurate data analysis and problem-solving.
4. Standardize (Seiketsu): Implement standardized processes for data collection, analysis, and improvement efforts. Develop standardized work instructions that define how tasks should be performed to maintain consistency.
5. Sustain (Shitsuke): Incorporate this principle into the Control stage of DMAIC to ensure the improvements are sustained over time. Establish processes for ongoing monitoring, auditing, and maintaining the organized and efficient work environment.

## Slide 15
SORT Sort out necessary and unnecessary items. The unnecessary items should be removed from the area. | Unnacceptable No evidence shown | Poor Only evident here and there | Good Applied and evident in most areas | Excellent Thoroughly evident and apply everywhere | World Class Always looking for ways to make even more improvements
1. Items/supplies on surfaces have been sorted, separating needed | 1 | 2 | 3 | 4 | 5
2. Items/supplies in bookcases or on shelves have been sorted, separating needed from unneeded | 1 | 2 | 3 | 4 | 5
3. Items in cupboards or drawers, including desk and file drawers, have been sorted, separating needed from unneeded | 1 | 2 | 3 | 4 | 5
4. Items on floors have been sorted, separating needed from unneeded eliminating floor piles and all cords are safely contained. | 1 | 2 | 3 | 4 | 5
5. Needed items have been placed at the closest location to where they are used the most to minimize the waste of motion. | 1 | 2 | 3 | 4 | 5
6. Unnecessary items have been removed from the work area | 1 | 2 | 3 | 4 | 5
7. Work agreements for the above are documented and all staff know where to find the agreements. | 1 | 2 | 3 | 4 | 5
Team:
Date:
Name:
5S Audit Form
Total score:

## Slide 16
SET IN ORDER A place for everything and everything in its place so it should be easy to find. | Unnacceptable No evidence shown | Poor Only evident here and there | Good Applied and evident in most areas | Excellent Thoroughly evident and apply everywhere | World Class Always looking for ways to make even more improvements
1. Locations of needed items are labeled and items are in correct locations. | 1 | 2 | 3 | 4 | 5
2. Required quantities for needed items are determined (par levels), including items in desk drawers and in bookshelves. | 1 | 2 | 3 | 4 | 5
3. Locations for movable items are labeled, and items are placed in correct locations (white board/ laminated card/label on wall can be used). | 1 | 2 | 3 | 4 | 5
4. Visual controls and indicators are established including: Posted map of area, including individual room maps. | 1 | 2 | 3 | 4 | 5
5. There is Labeling indicating contents of drawers and cupboards (a new person should be able to locate without assistance). | 1 | 2 | 3 | 4 | 5
Team:
Date:
Name:
5S Audit Form
Total score:

## Slide 17
SHINE Keep work area clean and ready to use. Inspect regularly to ensure sort and set in order are maintained. | Unnacceptable No evidence shown | Poor Only evident here and there | Good Applied and evident in most areas | Excellent Thoroughly evident and apply everywhere | World Class Always looking for ways to make even more improvements
1. Work areas and equipment are stocked and organized on a consistent basis according to 5S agreements and schedules. | 1 | 2 | 3 | 4 | 5
2. Members of the work group follow 5S agreements on a daily basis. | 1 | 2 | 3 | 4 | 5
3. Sources and frequency of 5S problems are documented as part of routine work by all staff. | 1 | 2 | 3 | 4 | 5
4. Surfaces are cleaned and clear of dust and debris. | 1 | 2 | 3 | 4 | 5
5. Checklists are utilized to identify ongoing Shine duties and the status of these are up‐to‐date. | 1 | 2 | 3 | 4 | 5
Team:
Date:
Name:
5S Audit Form
Total score:

## Slide 18
STANDARDIZE Maintain the first three S’s and have an awareness of improving neatness. | Unnacceptable No evidence shown | Poor Only evident here and there | Good Applied and evident in most areas | Excellent Thoroughly evident and apply everywhere | World Class Always looking for ways to make even more improvements
1. There is a 5S agreement in place and all employees know where it is located. | 1 | 2 | 3 | 4 | 5
2. . Leadership can explain why 5S is important. | 1 | 2 | 3 | 4 | 5
3. All staff can explain the importance of 5S. | 1 | 2 | 3 | 4 | 5
4. There is a standard process for training and orienting new staff to the 5S system | 1 | 2 | 3 | 4 | 5
5. There is a process in place to ensure unnecessary items do not “creep” back into the work area. | 1 | 2 | 3 | 4 | 5
Team:
Date:
Name:
5S Audit Form
Total score:

## Slide 19
SUSTAIN The 5S Discipline is embedded so that it becomes a way of life. 5S is no longer an event but routine. | Unnacceptable No evidence shown | Poor Only evident here and there | Good Applied and evident in most areas | Excellent Thoroughly evident and apply everywhere | World Class Always looking for ways to make even more improvements
1. 5S plans and action updates are clearly displayed and current. | 1 | 2 | 3 | 4 | 5
2. . Success stories are displayed and confirmed for improvement. | 1 | 2 | 3 | 4 | 5
3. Staff 5S roles are clearly identified. | 1 | 2 | 3 | 4 | 5
4. Department audits and subsequent improvement plans are displayed and current. | 1 | 2 | 3 | 4 | 5
5. Are work instructions and procedures available in the workplace regularly reviewed/kept up to date? | 1 | 2 | 3 | 4 | 5
6. Are display boards, activity charts, notice boards, etc. up to date and regularly checked? | 1 | 2 | 3 | 4 | 5
Team:
Date:
Name:
5S Audit Form
Total score:

## Slide 20
MEASURE
Data collection plan
Process Map
Histogram
Pareto Charts
Gemba walk
Tools
In this phase you:
Gather data from the process and determine the current quality level
Measure the existing system by defining valid and reliable metrics which will help in tracking progress towards the goal
Measure and monitors the project’s development and performance as soon as starting to work on it
Notes: Data Collection Plan: A structured document detailing how, when, and what data will be collected for analysis. It ensures accurate and consistent data gathering.
Process Map: A visual representation of a process's steps, inputs, outputs, and interactions, helping to identify inefficiencies and areas for improvement.
Histogram: A graph displaying data distribution through bars, helping to visualize patterns and variations in data.
Pareto Chart: A bar chart ranking data categories by frequency or impact, prioritizing the most significant issues for improvement.

## Slide 21: What good measurement looks like
Relevance: directly relate to the process or problem being analyzed.
Accuracy: must be precise and minimize errors.
Consistency: consistent across multiple trials or operators, ensuring reliable results.
Precision: provide sufficient detail to differentiate between variations.
Validity: accurately capture the aspect of the process being analyzed, reflecting the true state of affairs.
Reliability: consistently yield similar results over time and across different circumstances.
Completeness: cover all relevant aspects of the process without omitting critical data points.
Objective: unbiased and not influenced by personal opinions or interpretations.
Traceability: have a clear and documented path to the source data, ensuring transparency.
Measurable Units: expressed in standard units that are easily understood and compared.
Repeatable: Others should be able to replicate the measurements using the same methods and tools to verify results.
Traceable: Each measurement should be traceable back to its original source, ensuring data integrity.
Quantifiable: capable of being expressed numerically, allowing for quantitative analysis.

## Slide 22
1. Identify the questions
2. Data identification and listing
3. Understanding the type of data
4. Collect enough data
5. Choose measurement method
6. Sampling plan
7. Display the data
8. Data collection responsibility
DATA
COLLECTION PLAN
Notes: When building a data collection plan, make sure that:
You collect significant data
You collect valid data
All relevant data is collected simultaneously

## Slide 23: Basic LSS measurements
The goal of any improvement project is to make processes, products, or services:
Better: DPU, DPMO, RTY
Faster: Cycle Time
Cheaper: COPQ
Notes: Defects Per Unit (DPU): DPU is a metric that quantifies the number of defects found in each unit of a product or service. It's a measure of quality and is calculated by dividing the total defects by the total units produced. Reducing DPU is a key focus in LSS, as it signifies fewer defects and higher quality output.
Defects Per Million Opportunities (DPMO): DPMO is a normalized measure used to express defects in terms of a million opportunities. It's particularly useful when dealing with processes that have varying levels of complexity or different opportunities for defects. DPMO is calculated by multiplying DPU by 1,000,000 and dividing by the total opportunities for defects.
Rolled Throughput Yield (RTY): RTY is a metric that assesses the probability of producing defect-free units across multiple stages or processes. It considers the yield at each step of a process and calculates the cumulative probability of producing a good final product. RTY helps identify where defects accumulate and guides efforts to improve overall process yield.
Cycle Time: Cycle time is the duration it takes to complete a process from start to finish. It encompasses all the steps and delays involved in producing a product or delivering a service. Reducing cycle time is a key objective in LSS, as it leads to improved efficiency, faster delivery, and increased customer satisfaction.
Cost of Poor Quality (COPQ): COPQ represents the financial impact of poor quality processes on an organization. It includes both internal and external costs associated with defects, rework, scrap, customer complaints, warranty claims, and lost sales. Reducing COPQ is a primary goal in LSS to enhance process efficiency, reduce waste, and improve customer satisfaction.

## Slide 24: Process Map
Clearly Define Scope
Involve Stakeholders
Use Standard Symbols
Keep it Simple
Maintain Consistency
Sequence and Flow:
Use Descriptive Labels
Avoid Overloading
Consider Swimlane Diagrams
Validate with Stakeholders
Update Regularly
A Process Map is a valuable tool for gaining a clear understanding of the current state of a process.
To effectively use a Process Map :
Notes: The Process Map can bear some similarities with the Value Stream Map. A Process Map and a Value Stream Map (VSM) are both visual tools used in Lean Six Sigma to understand and improve processes, but they serve slightly different purposes and provide different levels of detail.
The Process Maps are typically used to analyze specific processes within a department or team. They help identify bottlenecks, inefficiencies, and opportunities for improvement within a localized process.
The VSM is a higher-level visualization that includes not only the processes but also the flow of materials, information, and value across the entire value stream. It provides a holistic view of how value is created and delivered to customers, covering the entire end-to-end process.
Clearly Define Scope: Clearly outline the boundaries and objectives of the process map to avoid including unnecessary details.
Involve Stakeholders: Collaborate with team members and stakeholders who are familiar with the process to ensure accuracy and completeness.
Use Standard Symbols: Follow standard flowchart symbols and shapes to represent different types of steps, decisions, inputs, and outputs.
Keep it Simple: Use a simple and intuitive design to ensure the process map is easily understood by everyone.
Maintain Consistency: Use consistent naming conventions and formatting for process steps, inputs, outputs, and symbols.
Sequence and Flow: Arrange steps in a logical sequence to reflect the actual flow of activities in the process.
Use Descriptive Labels: Provide clear and concise labels for each step and decision point to enhance understanding.
Avoid Overloading: Keep each step or activity focused on a single task. Avoid overloading a single step with too many details.
Consider Swimlane Diagrams: If there are multiple departments or roles involved, consider using swimlane diagrams to show responsibilities.
Validate with Stakeholders: Review the process map with relevant stakeholders to ensure accuracy and gather feedback.
Update Regularly: Processes evolve over time, so make sure to update the process map to reflect any changes.

## Slide 25
Source: lucidchart.com
Notes: Here you can see the examples of a process map for a manufacturing flow. This was created with Lucidchart: https://www.lucidchart.com/pages/templates
You can use various tools to create your own process map, from the simple Power Point to the more complex, dedicated ones.
The choice of tool depends on your familiarity with the software, the complexity of the process, and the level of detail you want to include. Regardless of the tool you use, the key is to ensure that the process map effectively communicates the sequence of steps, inputs, outputs, and interactions in the process.
Tools for Creating Process Maps:
Flowchart Software: Specialized flowchart software like Microsoft Visio, Lucidchart, Figma, Miro, allows you to create detailed and professional process maps with various shapes and connectors.
Microsoft PowerPoint: PowerPoint provides simple shapes and connectors that can be used to create basic process flow diagrams.
Pen and Paper: For simpler processes, you can draw a process map by hand on paper or a whiteboard.
Online Platforms: Some project management and collaboration platforms offer built-in tools for creating process maps.

## Slide 26: Defects per Unit (DPU)
Formula for Calculating DPU: DPU = Total Number of Defects / Total Number of Units
Example: Defects in Manufacturing
Let's say a manufacturing process produces 500 widgets, and during the production process, 75 defects are identified.
DPU = Total Number of Defects / Total Number of Units DPU = 75 defects / 500 units DPU = 0.15 defects per unit
Interpretation: In this example, the calculated DPU is 0.15, which means there are, on average, 0.15 defects per unit produced by the manufacturing process. This metric helps quantify the quality level of the product, and lower DPU values indicate higher product quality.
Notes: Defects Per Unit (DPU) is a key metric in quality management that measures the average number of defects found in each unit of a product or service. It helps quantify the level of defects present in the output of a process. Calculating DPU involves dividing the total number of defects by the total number of units produced.
Key Insights:
DPU is a valuable metric for assessing the quality of products or services in terms of defects.
It provides a quantitative measure of the level of defects present in each unit.
Monitoring and reducing DPU can lead to improved product quality and customer satisfaction.

## Slide 27: Defects Per Million Opportunities (DPMO)
Formula for Calculating DPMO: DPMO = (Total Number of Defects / Total Number of Units) × 1,000,000
Example: Defects in a Software Application
Let's consider a software application that undergoes testing for defects. In a batch of 10,000 lines of code, 25 defects are identified.
DPMO = (Total Number of Defects / Total Number of Units) × 1,000,000 DPMO = (25 defects / 10,000 units) × 1,000,000 DPMO = 2,500 DPMO
Interpretation: In this example, the calculated DPMO is 2,500, which means there are, on average, 2,500 defects per one million opportunities for defects in the software application's code. Lower DPMO values indicate better process performance and higher product quality.
Notes: Defects Per Million Opportunities (DPMO) is a standardized metric used in quality management to measure the rate of defects per one million opportunities for defects. It provides a way to compare defect rates across different processes or products with varying levels of complexity or different opportunities for defects. DPMO is particularly useful for benchmarking and analyzing the performance of processes.
Key Insights:
DPMO allows for standardizing defect rates across different processes or products.
It provides a more meaningful comparison of defect rates, considering the scale of opportunities for defects.
Monitoring and reducing DPMO can guide efforts to improve process performance and reduce defects.

## Slide 28: Rolled Throughput Yield (RPY)
Stage A
Stage B
Stage C
Units in = 100
Units W/O Rework = 90
RTY = 0.90
Units in = 90
Units W/O Rework = 80
RTY = 0.80
Units in = 80
Units W/O Rework = 75
RTY = 0.75
RTY = (Yield at Stage A) x (Yield at Stage B) x (Yield at Final Assembly) = 0.90 * 0.80 * 0.75 = 0.54 or 54%
Notes: Let’s break down Rolled Throughput Yield (RTY) with an example and the formulas used to calculate it.
Let's consider a manufacturing process that involves three stages to produce electronic components: Stage A, Stage B, and Final Assembly. Each stage introduces the possibility of defects. We want to calculate the RTY for the entire process.
Stage A: Initially, 100 units are processed in Stage A. Out of these, 90 pass the quality check, while 10 are rejected due to defects. The yield in Stage A is 90%.
Stage B: The 90 units from Stage A move to Stage B. Out of these, 80 pass the quality check, while 10 are rejected. The yield in Stage B is 80%.
Final Assembly: The 80 units from Stage B reach the Final Assembly stage. Out of these, 75 units are successfully assembled without defects, while 5 are found to be defective. The yield in the Final Assembly is 75%.
Now, let's calculate RTY:
RTY = (Yield at Stage A) x (Yield at Stage B) x (Yield at Final Assembly) = 0.90 * 0.80 * 0.75 = 0.54 or 54%
In this example, the RTY for the entire process is 54%, which means that there is a 54% probability of producing a defect-free unit from the initial 100 units that entered the process.
Formulas for RTY Calculation:
The formula to calculate RTY is straightforward and involves multiplying the yields at each stage of the process:
RTY = Yield at Stage 1 x Yield at Stage 2 x ... x Yield at Final Stage

## Slide 29: Cycle Time
Formula for Calculating Cycle Time: Cycle Time = Total Elapsed Time / Number of Cycles
Example: Manufacturing Cycle Time
Consider a manufacturing process that produces a specific product. The process consists of multiple steps, from raw material acquisition to finished product assembly. Let's say the total elapsed time for the manufacturing process is 120 hours, and during that time, 30 production cycles were completed.
Cycle Time = Total Elapsed Time / Number of Cycles Cycle Time = 120 hours / 30 cycles Cycle Time = 4 hours per cycle
Interpretation: In this example, the calculated cycle time is 4 hours per cycle. This means it takes an average of 4 hours to complete each production cycle in the manufacturing process. Lower cycle times indicate faster process execution and improved efficiency.
Notes: Cycle time is a fundamental metric in process improvement that measures the time it takes to complete a process or task from start to finish. It's a critical indicator of process efficiency, productivity, and customer responsiveness. Calculating cycle time involves measuring the time taken for each individual cycle or iteration of a process.
Key Insights:
Cycle time is a measure of process efficiency and effectiveness.
It helps identify bottlenecks, delays, and areas for improvement within a process.
Shortening cycle times often leads to reduced lead times, faster delivery, and improved customer satisfaction.

## Slide 30: Cost of Poor Quality (COPQ)
Formula for Calculating COPQ: COPQ = Internal Failure Costs + External Failure Costs + Appraisal Costs + Prevention Costs
Example: Manufacturing COPQ
Consider a manufacturing company that produces electronic devices. The COPQ components are as follows:
Internal Failure Costs: $10,000 (cost of rework, scrap)
External Failure Costs: $5,000 (warranty claims, returns)
Appraisal Costs: $2,000 (inspection, testing)
Prevention Costs: $3,000 (training, quality improvement initiatives)
COPQ = Internal Failure Costs + External Failure Costs + Appraisal Costs + Prevention Costs COPQ = $10,000 + $5,000 + $2,000 + $3,000 COPQ = $20,000
Interpretation: In this example, the calculated COPQ is $20,000. This represents the total cost incurred due to poor quality, including both tangible and intangible expenses. Reducing COPQ is a critical objective in process improvement to enhance efficiency, minimize waste, and increase customer satisfaction.
Notes: Cost of Poor Quality (COPQ) is a significant metric in quality management that quantifies the financial impact of defects, errors, and inefficiencies within a process. It encompasses both internal and external costs associated with poor quality, such as rework, scrap, customer complaints, warranty claims, and lost sales. Calculating COPQ involves identifying and summing up these various cost components.
Key Insights:
COPQ provides a comprehensive view of the financial impact of poor quality.
It motivates organizations to identify and eliminate sources of defects and waste.
Lowering COPQ contributes to higher profitability and improved customer experiences.

## Slide 31: Histogram
A Histogram is a graphical representation of data distribution, showing the frequency of data points within specified intervals or "bins."
It helps visualize the shape and spread of data, allowing you to understand the central tendency and variability.
Histograms are used to analyze continuous data, such as measurements or quantities.
They provide insights into the distribution of data, including information about modes, skewness, and outliers.
Notes: Creating a histogram helps you understand the variability and distribution of data. It aids in identifying potential areas of improvement and focusing efforts on addressing issues that affect the process's performance. By analyzing the histogram, you can make informed decisions about setting targets for improvement and identifying the root causes of any process-related problems. The histogram's insights contribute to data-driven decision-making and guide the subsequent stages of the Lean Six Sigma methodology.
Common tools for creating histograms include:
Microsoft Excel: Excel's built-in charting capabilities allow you to create histograms using the "Histogram" chart type.
Minitab: A statistical software commonly used in LSS, Minitab provides dedicated tools for creating histograms and performing statistical analysis.
Tableau: A data visualization tool that can be used to create interactive and visually appealing histograms.
Dot Plots: A dot plot is a simple chart that displays individual data points along an axis. It's useful for showing the distribution of data and identifying outliers. Tools for creating dot plots include:
Microsoft Excel: You can create dot plots in Excel using scatter plots with individual data points plotted along the axis.
R or Python: Programming languages like R or Python with libraries such as matplotlib or ggplot2 can be used to create customized dot plots.
Online Data Visualization Tools: Various online tools offer easy-to-use interfaces for creating dot plots without requiring programming skills.

## Slide 32: Pareto Charts
A Pareto Chart is a bar chart that combines both bar and line graphs to display data in descending order of frequency or importance.
It is used to prioritize problems or issues based on the Pareto Principle (80/20 rule), which suggests that a significant portion of the effects (80%) comes from a small number of causes 20%).
Pareto Charts help identify the vital few factors contributing to the majority of issues.
They are particularly effective for identifying areas of focus and prioritizing improvement efforts.
Notes: Pareto Graphs (Pareto Charts): A Pareto graph displays the relative frequency or count of different categories in descending order, emphasizing the most significant contributors.
Combination of a bar and line table that visualizez a set of data. Info can be related to cost, time and mistakes. It can measure the cumulative impact of defects. The cumulative impact is the result of a defect occurring over a long time. The pareto chart can also assist and offer a clear understanding of problems that must be addressed first which helps to deliberate and arrange for the right and necessary procedures or actions to be performed in the event of a fault.
Common tools for creating Pareto graphs include:
Microsoft Excel: Excel provides templates for creating Pareto charts that automatically sort and display data categories in descending order.
Minitab: Minitab offers a dedicated Pareto chart tool that allows you to analyze and visualize data in the Pareto format.
Tableau: You can create interactive Pareto charts in Tableau by arranging data categories in descending order and using bar charts.

## Slide 33: Gemba Walk
The Kaizen Cycle
The Kaizen Cycle is an iterative process for improving an aspect of your operations, products or services
There are a couple of key points to focus on when using this process:
  Involve everyone in the process
  Test bigger changes at small scale before wider rollout
  Standardize working practices to improve efficiency
  Rinse & Repeat
For succeeding in engaging employees, and to prioritize suggestions, a digital tool such as Viima can be very helpful.
To do a Gemba walk, you go where the real work happens. They are a great tool for managers. Here’s how to run one:
Go meet frontline employees: factory floor, customer service, maintenance…
Go unannounced and don’t plan questions in advance
Observe closely, be curious, ask questions to understand a) what’s going on and b) if employees could fix one (or a few) thing, what would that be, and why
Consider using other inquisitive tools, such as the five whys to truly understand why something happens
Notes: The Gemba Walk is a powerful tool for gaining practical insights and understanding the real-world dynamics of a process.
While it is particularly valuable in the Measure and Analyze stages, its impact can extend to the other stages of the DMAIC process, including providing context for improvement strategies and helping to verify the effectiveness of implemented changes during the Control stage.

## Slide 34
Plan the walk
Prepare the team
Observe the process
Choose a topic to focus on
Gather and analyze data
Decide on proceeding actions
The 6 steps of a Gemba walk
Gemba Walk – 3 rules
Go see. Observe up close how things are created and whether the reality in the field is aligned with the business objectives and expectations.
Ask why. Try to understand each steps, the ins and outs of the processes.
Act and show respect. Be mindful about the work of employees and show appreciation and genuine interest for what they do. The intention is not to “boss people around”.

## Slide 35
Start by choosing a topic you will focus on during your walk This provides a purpose and determines the kind of information you are after and ensures effective results. You don’t have to predefine the challenge, as your focus is to identify possible issues and challenging elements, but it’s important to be aware of the context beforehand.
Plan the walk Be strategic and proactive in your approach. For this, you need to prepare a set of questions you will ask, as well as a clear structure of the steps you will take, the areas you will visit and the intent for each of those.
Prepare the team While you don’t have to announce when it will take place, it’s important to inform employees about the Gemba walks, and their purpose. It’s not about testing them, but about learning and improvement. Similarly, if someone will join your walk, train them to know what to observe and what to pay attention to.
Observe the process The manager’s role is not to show how it’s done. Observe without interrupting people or correcting their behaviour. Your goal is not to intervene, but to simply learn, observe, analyze and take notes.
Gather and analyze data Once you have gathered all the information you can go back to the drawing board, analyze the findings and identify areas where teams can act.
Work on an action plan Include the steps to follow, and action required and communicate the findings to the teams. Then start over and prepare for the next Gemba walks to dig deeper or to explore new areas. It’s best to repeat these during different times of the week and of the day.
Gemba Walk – your checklist to get started

## Slide 36
1. What is the standard or process you are working on?
Work area :
Process analysis
Gemba Walk
1. Go and See
Process:
Observer:
Observation date:
Participants:
2. What is the purpose of this process?
3. What measures are in place to assess the success of the process?
4. What challenges impact the outputs of the process?
5. Do you have ready access to all the resources necessary for the process?
6. How do you think this process can be improved?
Problem solving
1. What kind of problems are you facing in your daily work?
2. Why is this a challenge?
3. What can we do to implement corrective action?
1. What is today’s priority and why?
2. Is there something you want to improve in your daily routine?
3. Is the information documented and up-to-date?
Continuous Improvement
Notes: You can add, remove or change questions according to your own environment, project and department
Additional things to observe during the walk:
  Who is responsible for the process?
  Was the production target met? If not, why?
  Do workers appear to be making unnecessary movements in their work?
  Are there any machine breakdowns?
  Are people following standards?
  Are standards up to date?
  Are standards present?
  Are materials available?
  Are processes documented?
  Are there any abnormal conditions?
  Is the process achieving its purpose and, if not, in what ways is it failing?
  What are potential causes of failures?
  Is there presence of defective products?
  Was corrective action put in place?
  Improvement questions/tasks assignments?

## Slide 37
Quantitative
Regression analysis
Histogram
Pareto Charts
Qualitative
Fishbone diagram
5 Whys
FMEA
XY Matrix
Tools
ANALYZE
In this phase you:
Locate the source of the issue
Figure out what causes it
Keep a close eye on the entire process along with the data
Assess the progress by making a list of difficulties and concerns that arise from the data and observations

## Slide 38: Regression Analysis
A statistical technique used to examine the relationship between one or more independent variables (also known as predictors or features) and a dependent variable (also known as the outcome or response variable).
It helps to understand how changes in the independent variables are associated with changes in the dependent variable.
The primary goal of regression analysis is to establish a mathematical equation that can predict the value of the dependent variable based on the values of the independent variables. This equation is known as the regression equation or model.
Notes: There are different types of regression analysis, including:
Linear Regression: In linear regression, the relationship between the independent variables and the dependent variable is assumed to be linear. The goal is to fit a straight line that best represents the relationship between the variables.
Multiple Regression: Multiple regression involves more than one independent variable. It helps to understand how multiple variables collectively influence the dependent variable.
Logistic Regression: Logistic regression is used when the dependent variable is categorical, such as binary (yes/no) or multiple categories. It predicts the probability of the occurrence of a certain event.
Polynomial Regression: Polynomial regression accommodates curved relationships by using higher-degree polynomial equations to fit the data.
Ridge and Lasso Regression: These are techniques used to address multicollinearity and overfitting issues in multiple regression models.
Regression analysis involves estimating the coefficients of the regression equation, which represent the strength and direction of the relationship between the variables. Statistical methods are used to assess the significance of these coefficients, determine the goodness of fit of the model, and validate its predictive capability.

## Slide 39: Regression Analysis
Several tools and software platforms can be used for regression analysis, depending on your familiarity with statistical software and the complexity of your analysis.
Some commonly used tools for regression analysis:
Microsoft Excel: Excel offers built-in functions for linear regression analysis. It's suitable for basic regression tasks and simple data sets.
Minitab: Minitab is a statistical software designed for quality improvement and data analysis. It provides user-friendly tools for regression analysis, including multiple regression and logistic regression.
IBM SPSS: SPSS is a comprehensive software for statistical analysis. It offers various regression analysis tools, including linear regression, logistic regression, and more.
Illustration of linear regression on a data set
Notes: When choosing a tool, consider factors such as your level of expertise, the complexity of your analysis, the availability of specific features you need, and your organization's preferred software environment.
To get a clearer picture of how this can be used, let's consider an example on how to use it to improve a manufacturing process.
Example: Improving Product Quality in a Manufacturing Process
Scenario: A manufacturing company produces a certain type of electronic component. They've been experiencing variations in the quality of the finished products, resulting in defects and customer complaints. The company wants to identify which process parameters are contributing to these variations and how they can be controlled to improve product quality.
Step 1: Data Collection: The company collects data on various process parameters such as temperature, pressure, and production speed. They also measure the quality of the finished products using a quality index that represents the number of defects per unit.
Step 2: Regression Analysis: The data collected is used to perform regression analysis. In this case, they decide to use multiple linear regression to understand how the process parameters (independent variables) impact the product quality (dependent variable). The regression equation they derive might look like this:
Quality = β₀ + β₁ × Temperature + β₂ × Pressure + β₃ × Production Speed + ε
Where:
β₀, β₁, β₂, β₃ are the coefficients of the regression equation.
ε represents the error term.
Step 3: Interpretation: The coefficients (β₁, β₂, β₃) in the regression equation indicate the relationship between the independent variables and the dependent variable. Positive coefficients indicate a positive relationship, and negative coefficients indicate a negative relationship. The size of the coefficient indicates the strength of the impact.
Step 4: Analysis and Action: After running the regression analysis, the company finds that temperature and pressure have significant impacts on product quality. Higher temperatures and pressures lead to lower product quality. Production speed, however, doesn't show a significant impact.
Step 5: Process Improvement: Armed with this information, the company takes action to improve the process. They implement tighter controls on temperature and pressure during the manufacturing process. As a result, they observe a significant reduction in defects and improved product quality.
Step 6: Continuous Monitoring: The company continues to monitor the process and collect data. They periodically re-run the regression analysis to ensure that the improvements are sustained and identify any new factors that might impact product quality.
In this example, regression analysis helped the manufacturing company identify the key process parameters affecting product quality. By making data-driven improvements based on the analysis, they were able to enhance their process and achieve better product quality, aligning with the principles of Lean Six Sigma.

## Slide 40: Fishbone Diagram
The fishbone diagram, also known as the Ishikawa diagram or cause-and-effect diagram, is a visual tool used in problem-solving and process improvement.
It helps identify the root causes of a specific problem or issue by breaking down potential causes into various categories.
The diagram resembles the skeleton of a fish, with the "head" representing the problem and the "bones" representing potential causes.
Notes: Creating a Fishbone Diagram:
Identify the Problem: Clearly define the problem you want to address and place it at the head of the diagram.
Identify Categories: Choose the relevant categories that could contribute to the problem. These will be the main "bones" of the fishbone.
Brainstorm Potential Causes: Under each category, brainstorm potential causes that might be linked to the problem. Encourage a diverse group of stakeholders to contribute ideas.
Analyze and Prioritize Causes: Evaluate the potential causes and identify the most likely ones. You can use tools like data analysis or the 5 Whys technique to delve deeper into the causes.
Draw the Diagram: Draw the fishbone diagram by connecting the categories (bones) to the problem statement (head) using diagonal lines. Label each "bone" with the potential causes you've identified.
Share and Collaborate: Display the fishbone diagram to your team or stakeholders. Discuss and refine the causes, and gather input on possible solutions.

## Slide 41
Root cause analysis: The fishbone diagram
The problem / Outcome
Environment
Equipment/Supplies
Rules(Policies/Procedures
Place
Systems
Staff/People
Project:
Date:
Notes: Components of a Fishbone Diagram:
Problem Statement (Head): This is the issue you want to analyze and solve. It is placed at the head of the fishbone diagram.
Categories (Bones): The main "bones" of the diagram represent different categories of potential causes that might contribute to the problem. Common categories include:
  Methods: Processes, procedures, or methods that could be causing the problem.
  Machines: Equipment, tools, or machinery that might be involved.
  Materials: Raw materials, ingredients, or supplies used in the process.
  Manpower: Human resources, skills, or training of the individuals involved.
  Measurement: Measurement systems or metrics that might be causing variations.
  Environment: Surrounding factors, conditions, or external influences.

## Slide 42
Define the problem:
Root cause problem:
1. (Symptom)
What is happening? What is causing it?
2. (Symptom)
3. (Symptom)
4. (Symptom)
5. (Symptom)
Why is that?
Why is that?
Why is that?
Why is that?
2. Ask Why
Root cause analysis: 5 Whys
Notes: Most problems are usually only a symptom of a larger, underlying issue, known as a root cause
The Five Whys is a great framework for finding these real root causes
You’ll find an example above, along with a table that can be used for documenting your problems
Using a systematic method, such as the table mentioned above for documenting these pathways, can help you identify repeating patterns in your processes that cause many issues and should be fixed as soon as possible

## Slide 43
Root cause analysis: 5 Whys – The tree framework
If there is more than one pathway and you identify more than one root cause, you can group several root causes under the tree framework.
Define the problem
Contributing factors #1
Contributing factors #2
Contributing factors #3

## Slide 44: FMEA – Failure Mode Effect Analysis
FMEA is a systematic process that requires thoughtful consideration for all of the potential failure mode associated with a new design or process.
FMEA helps teams proactively assess the impact of failures, prioritize them based on severity, and develop strategies to prevent or minimize their effects.
Before you get started with FMEA, establish the ground rules:
Define the scale you plan on using for Severity, Occurrence and Detection
Document any assumptions
Define your Acceptable Risk Level
Notes: Before you get started with FMEA, establish the ground rules:
Define the scale you plan on using for Severity, Occurrence and Detection. This is unique to your product, industry and sector. The severity scores can differ depending on the types of products you’re making.
Document any assumptions.
Define your Acceptable Risk Level. Every organization has a different appetite for risks, just like your customers have a different one. Define what is an acceptable level of risk for you to avoid biases that can creep in.

## Slide 45
Severity
Occurrence
Detection
Risk Priority Number
Action results
The FMEA – Failure Mode Effect Analysis
Notes: The 10 step process for an FMEA
Define you resisted or process and narrow the scope as much as possible.
Once you identified the scope, identify potential failure mode. A failure is a non-conformance, error or effect associated with your product. The failure mode tells you how something can go wrong, the method in which something could fail.
Determine the Effects: the impact on the end user or customer. When a process fails, what is the effect on the end user? This is what drives the severity score.
Estimate the Severity. This is a measure of the degree to which the end user is impacted by the potential failure mode being analysed. Here you define the scale in relationship to your own product and the severity of your specific unique failure modes.
Determine potential causes (here you can use the 5Whys or the fishbone diagram.
Estimate the Occurrence. The occurrence ranking is defined as the likelihood or probability that a failure will occur.
Determine the current Controls, which refers to anything in your process that might prevent or detect the failure mode that’s being analysed.
Estimate the Detection, which is the reflection of the capability and effectiveness of your process control strategy to identify a failure mode once it has occurred.
Calculate the Risk Priority Number (RPN), which gives an objective prioritisation tool to determine the “high risk” failure modes that we should focus on.
Take Corrective Action to mitigate risk

## Slide 46: X-Y Matrix – Prioritizing the root causes
A tool used to prioritise the potential strength of the relationship between input and process indicators (Xs) and the output indicators (Ys)
This is a subjective analysis tool that provides structure in team decision making. It’s used to decide what X data to collect.
To identify the X in the X-Y Matrix, you use data from three main sources:
process mapping
fishbone diagram
data analysis - graphs and statistics
Notes: An X-Y Matrix, is a tool used in Lean Six Sigma for identifying potential relationships or correlations between two different sets of data. It helps teams analyze whether changes in one variable might have an impact on another variable. The matrix is particularly useful for exploring cause-and-effect relationships and determining where to focus improvement efforts.

## Slide 47
2. List key output indicators
3. Potential input or process indicators
1. List key output indicators
4. Rate the effect or correlation of each input to output.
X-Y Matrix
5. Sort the results high to low
Notes: List the key output indicators across the top, horizontally. They should be relatively small number.
Assign a priority number for each Y, from 1 to 10, 10 being the most important. They indicate the relative importance to each other and should not be the same
Vertically, on the first column list all the potential input or process indicators X factors, that may affect any of the Ys. These are the brainstorm Xs from the fishbone diagrams. These are the brainstormed Xs from the fishbone diagrams. If there is a duplicate factor, just list it once.
Rate the effect or correlation of each input to output. For example, 0 = no correlation. 1 = little correlation. 3 = moderate correlation. 9 = stronger correlation. Cross multiply each rating by the importance and sum across putting the result in the last column
Finally, sort the results from high to low prioritising the X data to collect. Look for a natural break in the number of the scores to determine which Xs to collect data on. This would be 10 to 15 Xs.

## Slide 48
Brainstorming, idea generation & idea challenges
Design for Experiments (DOE)
How Might We Statements (HMW)
5S
Failure Mode Effect Analysis (FMEA)
Tools
IMPROVE
In this phase you:
Devise a plan to address the identified root causes
Proposing and choosing a solution to improve the system
Identify new methods to do things better, cheaper, faster
After figuring out the solutions, put them in action, track and measure the progress

## Slide 49: Brainstorming techniques
Brainstorm cards are a useful tool created by the Board of Innovation for coming up with dozens of new ideas related to whatever challenge or problem you are currently working with.
Brainstorm cards help you consider external factors such as: societal trends, new technologies, and regulation in the context of your business.
Read more: Idea Generation – Brainstorm Cards
Notes: Everything you should know about brainstorming, you can find in this article: https://www.viima.com/blog/brainstorming-guide

## Slide 50: Analogy thinking
Analogy thinking is a technique for using information from one source to solve a problem in another context. Often one solution to a problem or opportunity can be used to solve another problem.
Analogy thinking can, for example, be used for analyzing a successful business, identifying what makes it great, and then applying those same principles for your business. This is an effortless method for coming up with new ideas that are pre-validated.
You can use The Analogy Thinking Canvas to map your ideas.
Read more: Idea Generation – Analogy Thinking

## Slide 51: Opposite thinking
Opposite/reverse thinking is a technique that can help you question long-held assumptions related to your business.
It’s a useful tool to consider if you feel your team is stuck with the conventional mindset and coming up with those “out-of-the-box ideas” seems to be difficult.
Often, the best solutions aren’t found through a linear thought process. Although our brains are wired that way, aopposite thinking can help us question the norm.
With this type of thinking, you consider the exact opposite of what’s normal.
Read more: Idea Generation – Opposite Thinking

## Slide 52: Idea Challenges
An idea challenge is a focused form of innovation where you raise a desire, concern, or area of improvement with the hopes of finding creative solutions.
It usually starts off in the form of a question and is guided towards a specific audience, mandated by other preset parameters.
Idea challenges are a very versatile and useful in a variety of situations. By setting different specifications and parameters, you can customize idea challenges to fit a variety of different use cases.
Notes: You can read all about idea challenges, what they are, how to run one and best practices here: https://www.viima.com/blog/the-complete-guide-to-idea-challenges#types-of-idea-challenges
Or watch a summary of the information here: https://youtu.be/tB1GcjslTec If you're interested in running your very own idea challenge, feel free to download our Idea Challenge Toolkit.
https://www.viima.com/get-the-complete-toolkit-for-idea-challenges
The Toolkit consists of:
1. Slide templates for planning the process and communicating about it 2. Email templates that further help you communicate the right points 3. A modifiable copy of the Idea Challenge Canvas for planning the challenge

## Slide 53
Notes: Idea challenges are becoming increasingly popular because they let you harness the collective intelligence of hundreds or even thousands of people to focus on what matters most, which is the key to effectiveness.
It is a way of gathering collective creative input to find solutions to very specific matters.
These matters can vary all the way from complex strategic problems to simple enhancements to existing processes.
For example, a common use for idea challenges is to rally the entire organization around a strategic goal to focus on implementing it across all levels of the company.
The three key benefits of idea challenges have to do with: time, effectiveness, and communication.

## Slide 54: Design of Experiments (DOE)
DOE is a powerful data collection and analysis tool that can be used in a variety of experimental situations.
DOE allows for multiple input factors to be manipulated, determining their effect on a desired output (response). By manipulating multiple inputs at the same time, DOE can identify important interactions that may be missed when experimenting with one factor at a time.
When we think that more than one input factor might affect the output, DOE comes in handy. For instance, if we want to know how both temperature and pressure impact the strength of a glue bond.
DOE can also be used to confirm suspected input/output relationships and to develop a predictive equation suitable for performing what-if analysis.
Notes: Best Practices for Design of Experiments (DOE):
Clearly Define Objectives: Clearly understand what you want to achieve with the experiment and define your goals.
Identify Factors: Identify the key factors (variables) that might influence the outcome.
Select Appropriate Design: Choose the right experimental design based on the number of factors, levels, and interactions you want to study. Common designs include Full Factorial, Fractional Factorial, and Response Surface designs.
Randomization: Randomize the order of experiments to reduce bias and ensure results are not influenced by external factors.
Replicates: Conduct multiple trials for each combination of factors and levels to account for variability and improve reliability.
Control Variables: Keep non-study factors (variables) constant to isolate the effect of the factors you're testing.
Collect Accurate Data: Ensure data collection methods are accurate and consistent to avoid errors.
Statistical Analysis: Use appropriate statistical techniques to analyze the data and identify significant effects and interactions.
Interpret Results: Understand the implications of the analysis and draw meaningful conclusions.
Validation: Validate the results by conducting additional experiments or applying the optimized settings in a real-world scenario.

## Slide 55: Example
Factors and Levels:
Factor 1: Baking Temperature (Low, Medium, High)
Factor 2: Kneading Time (Short, Medium, Long)
Experimental Design:
Full Factorial Design (Test all combinations of factors and levels)
Experiment Setup:
Prepare batches of bread dough.
Apply the designated baking temperature and kneading time for each combination.
Data Collection:
After baking, gather taste testers to rate the texture and taste of each bread batch on a scale of 1 to 5 (1 being poor and 5 being excellent).
Test Plan for Bread Quality Improvement
Data Analysis:
Analyze the data to understand how baking temperature and kneading time affect texture and taste ratings. Look for patterns and significant effects.
Optimization:
Based on the analysis, determine the optimal combination of baking temperature and kneading time that leads to the highest texture and taste ratings.
Notes: Options and Variables in Conducting DOE:
Factors: These are variables that you're intentionally changing to see how they impact the outcome.
Levels: Different settings or values at which factors are tested.
Experimental Designs: Various designs like Full Factorial (tests all combinations), Fractional Factorial (tests a subset), and Response Surface (optimizes factors for desired outcomes).
Control Factors: Variables that you keep constant to isolate the effect of the factors you're studying.
Randomization: Randomly assigning the order of experiments to minimize bias.
Replicates: Repeating experiments multiple times to account for variability.
Blocking: Dividing experiments into groups to account for potential external influences.
Response Variables: The outcomes you're measuring and analyzing.
Interaction Effects: How factors might impact outcomes differently when combined.
Statistical Software: Tools like Minitab, JMP, or R for data analysis and visualization.

## Slide 56: How Might We Statements
HMW questions is a technique used to define solvable problems in design thinking or innovation cycles.
It turns declarative statements and uncertainties into questions that do not imply judgment or constrains, and do not hint at a solution. Instead, HMW questions provoke creative thinking and invite as many suggestions as possible.
HMW helps you define problems based on initial research or direct customer feedback. So, before you kick off a workshop or brainstorming sessions, make sure to have a solid knowledge base on challenges, issues or problems your organizations is facing.
Notes: HMW technique utilizes research results from your target audience research, journey mapping and empathy mapping, interviews, etc. Customers’ feedback can be turned into HMW questions too to troubleshoot problems and increase customer satisfaction.
The goal when using HMW technique is to spark creativity and imagination, without any implication of solution. And finally, the desired result is several HMW questions that can start a rich brainstorming session.
You can read more about HMW here: https://www.viima.com/blog/how-might-we

## Slide 57
1. Target audience research (TA). People are at the core of the HMW technique. Research your customers (users). This step will help you identify your customer’s (user’s) needs and pain points. Keep in mind that the HMW technique is meant to help create the best version of your product or service, and here the best means created for the target user.
2. Point of View (POV) statement. POV is a method to reshape challenges into actionable steps. It is a combination of your target audience, their needs, and insights (reasons behind their needs) uncovered during the research phase. Interaction Design Foundation offers the following formula for a POV statement:
3. Frame the challenge. With insights into your target audience and their challenges, narrow down the problem that your team will focus on. Anything that your TA addressed as challenging is worth improving and looking at as a target for an HMW session.
Steps to consider
TA (descriptive)
BECAUSE
INSIGHT (compelling)
NEED (verb)
NEEDS TO
Notes: Preparation Will Help to Ask the Right Questions that Are:
Productive: generates several possible approaches or solutions.
Accessible: people that aren’t experts in the area can offer a solution.
Not too broad: offers some direction to start solving the problem.
Not too narrow: does not limit ideas to a specific solution or approach.
Attainable: hints at reachable goals and even possible successful outcomes.
Outcome-oriented: helps explain what success would look like.
People-centered: always consider the person to whom you are innovating.

## Slide 58
Pet owner.
Tourist.
Innovation manager.
Person interested in sustainable produce.
Marketing professional.
Librarian.
…
Needs an access to the history of their pet’s veterinary care information.
Needs access to public transportation tickets.
Needs a place that would help them with handling employee yearly feedback.
…
Team/Name
1. Target Audience
2. Their Needs
HMW Questions: Turn POV Challenges into Opportunities
Pet owner loves their pet and want to be on time for their recommended check-up, but they cannot find the paper reference written by the vet during the last visit.
City visitors feel compelled to take taxis, which are very expensive, because they don’t know how to buy public transportation ticker nor if the short-term tickets even exist.
…
3. Insights
Notes: Avoid Common Mistakes!
Don’t ask questions that are too narrow and hint at one possible solution.
I.e. How Might We make a better website by making homepage’s visuals higher quality
2. Don’t ask questions that are too broad and do not focus on a particular challenge.
I.e. How Might We make a better website?
3. Don’t bulk up few questions into one and make it difficult to point point a solution.
I.e. How Might We make a better, faster and more beautiful website?

## Slide 59
How Might We [action] [do what] so that [TA] [insight].
How Might We create [action] an easy method to collect and store information related to our treated animals [do what], so that pet owners [TA] could check the information without calling us and saving their/our time?
How Might We…
so that…
How Might We…
so that…
How Might We…
so that…
Team/Name
HMW Questions: Template
How Might We…
so that…
How Might We…
so that…
How Might We…
so that…
Recommended formula:
How Might We…
so that…
Notes: The purpose of the HMW session is to set the attainable goals and a clear direction for your design or innovation process.
Go through all submissions, discuss them with people present, and ask them to vote on the most feasible (financially beneficial, easiest to implement, etc.), ideas.
Select and prioritize a handful of HMWs your team will work on (two to five). These will be your core problems that you will tackle in the next steps of the process.
Ideate and brainstorm creative and out-of-the-box solutions that are worthy to try out and move to prototyping (and then testing) steps.
Do not remove unselected ideas!
Creative ideas do not have a date of expiration and you never know when something might become just the right solution for your future problems.

## Slide 60
How Might We [action] [do what] so that [TA] [insight].
How Might We create [action] an easy method to collect and store information related to our treated animals [do what], so that pet owners [TA] could check the information without calling us and saving their/our time?
How Might We…
so that…
How Might We…
so that…
How Might We…
so that…
Team/Name
HMW Questions: Template
How Might We…
so that…
How Might We…
so that…
How Might We…
so that…
Recommended formula:
How Might We…
so that…
Notes: The purpose of the HMW session is to set the attainable goals and a clear direction for your design or innovation process.
Go through all submissions, discuss them with people present, and ask them to vote on the most feasible (financially beneficial, easiest to implement, etc.), ideas.
Select and prioritize a handful of HMWs your team will work on (two to five). These will be your core problems that you will tackle in the next steps of the process.
Ideate and brainstorm creative and out-of-the-box solutions that are worthy to try out and move to prototyping (and then testing) steps.
Do not remove unselected ideas!
Creative ideas do not have a date of expiration and you never know when something might become just the right solution for your future problems.

## Slide 61
Control Plan
Statistical Process Control (SPC) charts
Standard Operating Procedures (SOP)
Tools
CONTROL
In this phase you:
Ensure that the changes will last and problems will not occur again
Any deviation should be recorded and brought to the attention of the team
Control strategy to monitor the ongoing performance
Notes: In the Control Phase of the DMAIC methodology in Lean Six Sigma, the focus is on implementing measures to sustain the improvements made in the earlier stages and prevent the recurrence of issues. Several tools are used to ensure that the process remains in control and continues to meet the desired standards.
We will cover here three tools, but keep in mind that there are many other tools you can choose from, depending on your needs. These are some of the tools you can choose from:
Visual Management: Involves using visual cues like charts, graphs, and color-coded indicators to quickly assess process status. A factory floor might use visual management tools to display real-time production data and highlight any deviations from target values.
Poka-Yoke (Mistake-Proofing): Implements mechanisms or devices that prevent errors from occurring in the first place. This tool reduces the likelihood of defects by making it impossible or difficult to make mistakes. In an assembly line, a poka-yoke device might ensure that parts are assembled correctly before moving to the next step.
Feedback Systems: Establishes a mechanism for gathering and using feedback from employees, customers, and other stakeholders to identify issues and make necessary improvements. An online retailer might use customer feedback to continuously enhance its website's user experience.
Documentation and Training: Ensures that processes, procedures, and improvements are documented and communicated effectively to relevant stakeholders. Regular training sessions are conducted to keep employees updated on the latest procedures. A hospital might provide training on the updated patient discharge process to ensure smooth implementation.
Project Reviews: Regularly scheduled reviews to assess the ongoing effectiveness of process improvements and identify areas for further enhancement. A software development team might hold monthly reviews to assess the impact of coding quality improvements on bug rates.

## Slide 62: Control Plan
During the Control Phase, the Control Plan ensures that the improvements made in the earlier phases are integrated into the day-to-day operations. It provides a systematic approach to monitor, manage, and respond to any potential issues that may arise.
The Control Plan should include the following elements:
Key Process Steps
Measurement and Monitoring
Frequency of Monitoring
Responsibilities
Control Limits and Targets
Actions and Responses
Documentation
Notes: Control Plan: A structured document that outlines the procedures, measurements, and actions required to maintain process improvements. It serves as a guide for ongoing monitoring and management. For example, a manufacturing company might use a Control Plan to ensure that product specifications are consistently met after process improvements.
The elements of a control plan:
Key Process Steps: Clearly define the critical steps of the process that need to be monitored and controlled.
Measurement and Monitoring: Specify the metrics and measurements that will be used to monitor process performance. This may include variables, attributes, or key performance indicators.
Frequency of Monitoring: Determine how often measurements will be taken, whether it's continuously, periodically, or after specific events.
Responsibilities: Assign roles and responsibilities for monitoring and managing the process. Identify who is responsible for taking measurements, analyzing data, and taking corrective actions.
Control Limits and Targets: Define the acceptable range of values for each metric. Control limits ensure that the process stays within acceptable boundaries.
Actions and Responses: Detail the actions to be taken if the process goes out of control or if deviations from the target occur. This can include escalating issues, implementing corrective actions, and involving relevant stakeholders.
Documentation: Maintain a record of measurements, actions taken, and any changes made to the process. This documentation serves as a historical record and supports future improvements.

## Slide 63
Notes: A control plan is an example of a quality control strategy. The control plan must be implemented after creating a new process or after improving an existing process. It helps to ensure that the staff correctly monitors the new and improved processes.
Header Block
Reference Number
This is for the control plan itself – control plans can change, independent of drawing specifications. It is important to maintain revision control and to ensure that the lates revision is being used everywhere.
Revision Date:
Revision date for the control plan itself.
Part Number:
Engineering drawing or part number that contains the relevant specifications.
Approval Blocks:
Responsible parties should sign off on the control plan. This will prevent confusion in the future, should quality issues arise.
Process Name / Operation
Ref #
Normally links back to the process step # in the process flow chart.
Process Name
Note what is happening during this process step
Safety Plan
Keep any special notations in this column relative to criticality. Safety or critical-to-quality specifications are the top priority in any control plan.
Specifications and Controls
Specification / Tolerance
Note the engineering specification, as stated on the drawing, along with the tolerance.
Evaluation / Measurement
This is the method for measuring or otherwise evaluating the product/process to ensure that the specification is met.
Sampling Requirement
How frequently the measurement will take place. Sampling requirements are usually time based
Control method:
This column summarizes how the process is controlled, in order to deliver an in-specification result for the given spec.
Reaction Plan:
The reaction plan describes what must happen if an out-of-specification condition is found. This is about containing the situation to ensure that defective product does not reach the customer. The depth of the containment plan depends on the severity of the defect.

## Slide 64: Statistical Process Control (SPC) Charts
A documented set of step-by-step instructions, guidelines, or protocols that outline how a specific task, process, or activity should be performed within an organization.
Any process has Causes of Variation known as:
Common Causes: natural variability
Special Causes: unnatural variability
  Assignable: The reason for the detected variability
  Pattern Change: The presence of trends or
unusual patterns
SPC is a basic tool for monitoring and improving process variation.
SPC is used to detect the variation given by Special Causes and tells us if the process is "out of control", but it does NOT tell us why.
SPC is a visual management tool.
Notes: Statistical Process Control (SPC): Utilizes statistical techniques to monitor the stability of a process and detect any potential deviations from the desired outcomes. Control charts are commonly used in SPC to track process performance over time. For instance, a semiconductor manufacturing plant might use control charts to monitor the thickness of wafer coatings.

## Slide 65: Choosing the SPC charts
Notes: Statistical Process Control (SPC) charts, also known as control charts, are used to monitor and control the variation in a process over time. There are several types of SPC charts, each designed to monitor specific types of data and variations. Some common types of SPC charts include:
X-bar and R Charts: These charts are used to monitor the central tendency (average) and variability (range) of a continuous data process. The X-bar chart displays the average of sample means, while the R chart displays the range of sample ranges.
X-bar and S Charts: Similar to X-bar and R charts, these charts monitor the average and variability of a continuous data process. Instead of using ranges, the X-bar and S charts use the standard deviation of sample data.
Individuals (I-MR) Chart: Used when collecting data one observation at a time, the Individuals or I-MR chart tracks the individual data points (I-chart) and the moving ranges between consecutive data points (MR-chart).
P Chart: The P chart is used to monitor the proportion of defective items in a sample. It's suitable for attribute data that can be categorized as "defective" or "non-defective."
NP Chart: Similar to the P chart, the NP chart monitors the number of defective items in a fixed-size sample, making it suitable for attribute data.
C Chart: The C chart monitors the number of defects per unit in a sample. It's used for attribute data where the number of defects can vary within a fixed unit size.
U Chart: The U chart monitors the number of defects per unit in a variable-size sample. It's suitable for attribute data when the unit size varies.
EWMA Chart (Exponentially Weighted Moving Average): The EWMA chart is used to detect small shifts in a process. It places more weight on recent data points and is effective for detecting gradual changes.
CUSUM Chart (Cumulative Sum): The CUSUM chart is used to detect small shifts in a process over time. It accumulates deviations from the target or mean value and is useful for detecting process shifts early.
Z-MR Chart: This chart is used when data collected in subgroups don't follow a normal distribution. It combines a Z-chart (for averages) with an MR-chart (for ranges).
The choice of which SPC chart to use depends on the type of data being monitored (continuous or attribute), the nature of the process, and the specific goals of the monitoring effort. Different charts are suited for different situations, and selecting the appropriate chart is essential for effective process control and improvement.

## Slide 66: Standard Operating Procedure (SOP)
How it Works:
Documentation: step-by-step instructions for carrying out a process. It includes details on roles, responsibilities, required resources, and specific actions to be taken.
Training: training new employees or team members. They help ensure that everyone is trained consistently and follows the same procedures.
Consistency: maintain consistency and reduce variations in process execution. This consistency contributes to improved quality and reduced errors.
Reference: SOPs serve as a reference for employees to consult when performing a task. They can refer to the document for guidance, reducing the need for constant supervision.
Notes: "SOP" stands for "Standard Operating Procedure." An SOP is a detailed and documented set of step-by-step instructions that outlines how a specific task or process should be executed within an organization. It serves as a standardized guide to ensure that processes are carried out consistently and efficiently, leading to predictable and high-quality outcomes.
In the DMAIC framework, an SOP plays a crucial role, especially in the Control phase, where the focus is on maintaining the improvements made during the Improve phase. An SOP helps ensure that the process remains in control and that the gains achieved through process improvement efforts are sustained over time. It provides a clear reference for employees to follow, minimizing variations and reducing the chances of errors or deviations.

## Slide 67: Best Format for an SOP
Title: Clearly state the name of the process or task the SOP is addressing.
Objective: Explain the purpose of the process and what the desired outcome is.
Scope: Define the boundaries of the process and what is covered by the SOP.
Step-by-Step Instructions: Provide a detailed breakdown of each step in the process, including what needs to be done, who is responsible, and any required resources.
Visual Aids: Incorporate diagrams, flowcharts, or images to enhance understanding, especially for complex processes.
Roles and Responsibilities: Clearly define the roles of each team member involved in the process.
Safety Considerations: Include any safety precautions that need to be followed during the process.
References: Cite any relevant documents, guidelines, or regulations that should be consulted.
Approval and Revision History: Indicate who has approved the SOP and provide a record of any updates or revisions.
Contact Information: Include contact information for questions or clarifications.
An effective SOP should be clear, concise, and easy to understand. It should include the following elements:
Notes: The best format for an SOP varies depending on the organization's preferences and guidelines, but it should always prioritize clarity, accuracy, and usability.

## Slide 68: Choosing the SOP format
Use Case:
Staightforward
Small scope
Components:
Statement of purpose or introduction
Summary or overview
Details or step by step instructions
3-5 sections
Responsible
Use Case:
Complex
Large scope
Components:
Statement of purpose
Table of contents
Summary or overview
Details or step by step instructions
Multiple sections
Responsible
Use Case:
Simple or complex
Flexible scope
Components:
Statement of purpose or introduction
Easy to follow flowchart or diagram
Responsible
Simple
Hierarchical
Flowchart

## Slide 69: About Viima
We’re on a mission to help organizations make more innovation happen.
Viima is the all-in-one innovation platform that helps you go from ideas to innovations, every step of the way.
Getting started is fast and easy and the best part is that Viima is completely free for an unlimited number of users!
So, If you’re looking for a tool that can help you run and manage all your continuous improvement processes with ease, you can get started in as little as 5 minutes at viima.com.
START FOR FREE